## Slide 1: Wireless world in NS
Padma Haldar
USC/ISI

## Slide 2: Outline
Introduction
  Wireless basics
  Wireless internals
Ad hoc routing
Mobile IP
Satellite networking
Directed diffusion

## Slide 3: Contributions to mobility in ns
Original mobility model in ns contributed by CMU’s Monarch group
Other major contributions from UCB, Sun microsystems, univ of cincinnati, ISI etc
Other contributed models (not integrated) in wireless ns includes Blueware, BlueHoc, Mobiwan, GPRS, CIMS etc

## Slide 4: Wireless model
Mobilenode at core of mobility model
Mobilenodes can move in a given topology, receive/transmit signals from/to wireless channels
Wireless network stack consists of LL, ARP, MAC, IFQ etc
Allows simulations of multi-hop ad hoc networks, wireless LANs, sensor networks etc

## Slide 5: Wireless Example for ad hoc routing
Scenario
  3 mobile nodes
  moving within 670mX670m flat topology
  using DSDV ad hoc routing protocol
  Random Waypoint mobility model
  TCP and CBR traffic
ns-2/tcl/ex/wireless-demo-csci694.tcl

## Slide 6: An Example – Step 1
# Define Global Variables
# create simulator
set ns [new Simulator]
# create a flat topology in a 670m x 670m area
set topo [new Topography]
$topo load_flatgrid 670 670

## Slide 7: An Example – Step 2
# Define standard ns/nam trace
# ns trace
set tracefd [open demo.tr w]
$ns trace-all $tracefd
# nam trace
set namtrace [open demo.nam w]
$ns namtrace-all-wireless $namtrace 670 670

## Slide 8: GOD (General Operations Director)
Stores smallest number of hops from one node to another
Optimal case to compare routing protocol performance
Automatically generated by scenario file
set god [create-god <no of mnodes>]
$god set-dist <from> <to> <#hops>

## Slide 9: Example –Step 3
Create God
  set god [create-god 3]
  $ns at 900.00 “$god setdist 2 3 1”

## Slide 10: An Example – Step 4
# Define how a mobile node is configured
$ns node-config \
-adhocRouting DSDV \
-llType LL \
-macType Mac/802_11 \
-ifqLen 50 \
-ifqType Queue/DropTail/PriQueue \
-antType Antenna/OmniAntenna \
-propType Propagation/TwoRayGround \
-phyType Phy/WirelessPhy \
-channelType Channel/WirelessChannel \
-topoInstance $topo
-agentTrace ON \
-routerTrace OFF \
-macTrace OFF

## Slide 11: An Example – Step 5
# Next create a mobile node, attach it to the channel
set node(0) [$ns node]
# disable random motion
$node(0) random-motion 0
# Use “for” loop to create 3 nodes:
for {set i < 0} {$i < 3} {incr i} {
set node($i) [$ns node]
$node($i) random-motion 0
}

## Slide 12: Mobilenode Movement
Node position defined in a 3-D model
However z axis not used
  $node set X_ <x1>
  $node set Y_ <y1>
  $node set Z_ <z1>
  $node at $time setdest <x2> <y2> <speed>
Node movement may be logged

## Slide 13: Scenario Generator: Movement
Mobile Movement Generator
  setdest -n <num_of_nodes> -p pausetime -s <maxspeed> -t <simtime> -x <maxx> -y <maxy>
  Source: ns-2/indep-utils/cmu-scen-gen/setdest/
Random movement
  $node random-motion 1
  $node start

## Slide 14: A Movement File
$node_(2) set Z_ 0.000000000000
$node_(2) set Y_ 199.373306816804
$node_(2) set X_ 591.256560093833
$node_(1) set Z_ 0.000000000000
$node_(1) set Y_ 345.357731779204
$node_(1) set X_ 257.046298323157
$node_(0) set Z_ 0.000000000000
$node_(0) set Y_ 239.438009831261
$node_(0) set X_ 83.364418416244
$ns_ at 50.000000000000 "$node_(2) setdest 369.463244915743 170.519203111152 3.371785899154"
$ns_ at 51.000000000000 "$node_(1) setdest 221.826585497093 80.855495003839 14.909259208114"
$ns_ at 33.000000000000 "$node_(0) setdest 89.663708107313 283.494644426442 19.153832288917"

## Slide 15: Scenario Generator: Traffic
Generating traffic pattern files
  CBR/TCP traffic
  ns cbrgen.tcl [-type cbr|tcp] [-nn nodes] [-seed seed] [-mc connections] [-rate rate]
  CBR traffic
  ns cbrgen.tcl –type cbr –nn 20 –seed 1 –mc 8 - rate 4
  TCP traffic
  ns cbrgen.tcl –type tcp -nn 15 -seed 0 –mc 6
Source: ns-2/indep-utils/cmu-scen-gen/

## Slide 16: A Traffic Scenario
set udp_(0) [new Agent/UDP]
$ns_ attach-agent $node_(0) $udp_(0)
set null_(0) [new Agent/Null]
$ns_ attach-agent $node_(2) $null_(0)
set cbr_(0) [new Application/Traffic/CBR]
$cbr_(0) set packetSize_ 512
$cbr_(0) set interval_ 4.0
$cbr_(0) set random_ 1
$cbr_(0) set maxpkts_ 10000
$cbr_(0) attach-agent $udp_(0)
$ns_ connect $udp_(0) $null_(0)
$ns_ at 127.93667922166023 "$cbr_(0) start"
…….

## Slide 17: An Example – Step 6
# Define node movement model
source <movement-scenario-files>
# Define traffic model
source <traffic-scenario-files>

## Slide 18: An Example – Step 7
# Define node initial position in nam
for {set i 0} {$i < 3 } { incr i} {
$ns initial_node_position $node($i) 20
}
# Tell ns/nam the simulation stop time
$ns at 200.0 “$ns nam-end-wireless 200.0”
$ns at 200.0 “$ns halt”
# Start your simulation
$ns run

## Slide 19: Energy Extension
Node is energy-aware
Define node by adding new options:
$ns_ node-config \
–energyModel EnergyModel
    -initialEnergy 100.0
    -txPower 0.6
    -rxPower 0.2

## Slide 20: nam Visualization
Use nam to visualize:
  Mobile node position
  Mobile node moving direction and speed
  Energy consumption at nodes (color keyed)

## Slide 21: nam Visualization
Replace
$ns namtrace-all $fd
with
$ns namtrace-all-wireless $fd
At the end of simulation, do
$ns nam-end-wireless [$ns now]

## Slide 22: Outline
Introduction
  Wireless basics
  Wireless internals
Ad hoc routing
Mobile IP
Satellite networking
Directed diffusion

## Slide 23: Wireless Internals
Mobilenode
  Basic node that has address and port de-muxes, routing agent etc
  Stack of network components consisting of LL, MAC, NetIF radio-model etc
Wireless channel

## Slide 24: Portrait of A Mobile Node
Node
ARP
Propagation and antenna models
MobileNode
LL
MAC
PHY
LL
CHANNEL
LL
MAC
PHY
Classifier: Forwarding
Agent: Protocol Entity
Node Entry
LL: Link layer object
IFQ: Interface queue
MAC: Mac object
PHY: Net interface
protocol
agent
routing
agent
addr
classifier
port
classifier
255
IFQ
IFQ
defaulttarget_
Radio propagation/
antenna models
Prop/ant
Notes: droped: LL (1 packet only, drop due to arp), IFQ
MAC: collision detection
PHY: Carier Sense threshold, Receive Threshold. Packets above CSThresh are able to cause a collision.
IFQ: can be any queue, droptail or priority, etc.

## Slide 25: Mobile Node : Components
Classifiers
  defaulttarget_ points to routing agent object
  255 is the port id assigned for rtagent_
Routing agent
  May be ad hoc routing protocol like AODV, DSDV or directed diffusion

## Slide 26: Mobile Node: Components
Link Layer
  Same as LAN, but with a separate ARP module
  Sends queries to ARP
ARP
  Resolves IP address to hardware (MAC) address
  Broadcasts ARP query
Interface queue
  Gives priority to routing protocol packets
  Has packet filtering capacity
Notes:   Single buffer for a given unknown destination
  Inserts packet into interface queue

## Slide 27: Mobile Node: Components
MAC
  802.11
    IEEE RTS/CTS/DATA/ACK for unicast
    Sends DATA directly for broadcast
  SMAC (work in progress)
Network interface (PHY)
  Used by mobilenode to access channel
  Stamps outgoing pkts with meta-data
  Interface with radio/antenna models
Notes: Receiving and transmission energy

## Slide 28: Mobile Node: Components
Radio Propagation Model
  Friss-space model – attenuation at near distance
  Two-ray ground reflection model for far distance
  Shadowing model -probabilistic
Antenna
  Omni-directional, unity-gain

## Slide 29: Wireless Channel
Duplicate packets to all mobile nodes attached to the channel except the sender
It is the receiver’s responsibility to decide if it will accept the packet
  Collision is handled at individual receiver
  O(N2) messages  grid keeper, reference-copying etc

## Slide 30: Grid-keeper: An Optimization

## Slide 31: Mobile Node: Misc.
Energy consumption model for sensor networks
Visualization of node movement, reachability, and energy
Validation test suites

## Slide 32: Wireless Trace Support
Original cmu trace format
A separate wireless trace format developed later at ISI
Current ongoing effort to have ONE format to combine all wired and wireless formats

## Slide 33: Ad Hoc Routing
Four routing protocols currently supported:
  DSDV
    Contributed by CMU
  DSR
    Contributed by CMU; recently updated
  AODV
    Recently updated version from univ. of cincinnati;
  TORA
    Contributed by CMU
Examples under tcl/test/test-suite-wireless- { lan-newnode.tcl, lan-aodv.tcl, lan-tora.tcl }

## Slide 34: A Brief on MobileIP Support
Developed by Sun
  Require a different Node structure than MobileNode
  Co-exists with wired world in ns
Wired-cum-wireless extension
  Base-stations, support hier-rtg
Standard MobileIP
  Home Agent, Foreign Agent, MobileHosts
Example
  Under tcl/test/test-suite-wireless-lan-newnode.tcl (tests: DSDV-wired-cum-wireless and DSDV-wireless-mip)

## Slide 35: A Brief on Satellite Networking
Developed by Tom Henderson (UCB)
Supported models
  Geostationary satellites: bent-pipe and processing-payload
  Low-Earth-Orbit satellites
Example: tcl/ex/sat-*.tcl and tcl/test/test-suite-satellite.tcl

## Slide 36: A Brief on Directed Diffusion
Developed by SCADDS group at USC/ISI
Diffusion model in ns consists of
  A core diffusion layer
  A library of APIs for diffusion applications
  Add-on filters (for gradient routing, logging, tagging, srcrtg, GEAR etc)
Much in development
Source code in ~ns/diffusion3
Examples under tcl/ex/diffusion3 and test/test-suite-diffusion3.tcl

## Slide 37: SMAC
SMAC – MAC designed for sensor networks
Similar RTS/CTS/DATA/ACK like 802.11
Additional sleep-wakeup cycles
Reduce energy consumptions during idle phases
Much in development
Examples under tcl/test/test-suite-smac.tcl

## Slide 38: Summary
Wireless support in ns continuously evolving
Directed diffusion and SMAC – work in progress
Other contributed models (not integrated into ns distribution) :
  Mobiwan, GPRS, Bluehoc and blueware, CIMS etc
  Find at ns’ contributed code page at http://www.isi.edu/nsnam/ns/ns-contributed.html