## Slide 1: 2nd European ns-2 Workshop
Polly Huang
ETH Zurich
http://www.tik.ee.ethz.ch/~huang
April 18 & 19, 2001

## Slide 2: Workshop Overview
Welcome
Gratitude
Audience background
  object-oriented programming?
  tcl?
  use ns-2 before?
  tcl, c, or both?
  research interest?

## Slide 3: Workshop Intensity
Intended audience
  try to cover a wide range
  researchers, developers, educators
Cover
  both API & internal
  some could be too easy or too difficult
  see them as review or preview

## Slide 4: Schedule: Today
  9-9.50 overview/intro/essential/getting started
  10-10.50 tcl/otcl/ns-2 fundamentals
  11-11.50 examples - TCP, RED, multicast, web, wireless
  Lunch break
  1.30-2.20 lab 1 setup/running examples
  2.30-3.20 lab 2 tcl/otcl exercises
  3.30-4.20 lab 3 simple ns-2 exercise
  4.30-5.00 discussion/feedback

## Slide 5: Schedule: Tomorrow
  9-9.50 recap/wired internal
  10-10.50 wireless internal/making changes
  11-11.50 extending ns-2/case studies
  Lunch break
  1.30-2.20 lab 4 intermediate ns-2 exercise
  2.30-3.20 lab 5 getting data you want
  3.30-4.20 lab 6 advanced topic (TBD)
  4.30-5.00 discussion/feedback

## Slide 6: Outline: This Morning
Introduction
  the project, the software, the philosophy
  software architecture
  installation and getting started
tcl/otcl/ns-2 fundamentals
  programming tcl/otcl
  programming ns-2 simulation scripts
Example scripts
  TCP, web traffic, RED, multicast, wireless

## Slide 7: The VINT Project
Virtual InterNet Testbed
  a common platform for network research
  focus on multi-protocol interactions and scale
  http://netweb.usc.edu/vint
Follow-up projects
  SAMAN: scenario and performance
  CONSER: educational use

## Slide 8: Multi-state collaboration
AT&T Research
Lawrence Berkeley National Laboratory
UC Berkeley
USC/ISI
Xerox PARC
ETH TIK

## Slide 9: VINT People
Project leads and co-PIs
  Lee Breslau (AT&T Labs-Research)
  Deborah Estrin (USC/ISI)
  Kevin Fall (UC Berkeley)
  Sally Floyd (AT&T/ACIRI)
  Mark Handley (AT&T/ACIRI)
  John Heidemann (USC/ISI)
  Scott Shenker (AT&T/ACIRI)
Graduate students and staff members

## Slide 10: Project Goal
To support collaborative simulation effort
  promote sharing
    incorporate recent simulation models
  increase confidence in results
    establish regression test suite
  establish common reference
    current and periodic availability of source code
Base software is ns-2

## Slide 11: ns-2
Discrete event simulator
Packet level
Link layer and up
Wired and wireless

## Slide 12: Development Status
Columbia NEST
UCB REAL
ns-1
ns-2
  100K lines of C++ code
  70K lines of otcl support code
  30K lines of test suites
  20K lines of documentation

## Slide 13: Usage and Releases
Users from approximately
  600 institutes
  50 countries
Releases
  periodic official releases
  nightly snapshots (probably compiles and works, but buyers beware)
  available from USC/ISI or UK mirror

## Slide 14: Platforms
Most UNIX and UNIX-like systems
  FreeBSD or *BSD
  Linux
  Sun Solaris
  HP, SGI
Window 95/98/NT...
Emulation only for FreeBSD for now

## Slide 15: First Words of Caution
While we have considerable confidence in ns, ns is not a polished and finished product, but the result of an ongoing effort of research and development. In particular, bugs in the software are still being discovered and corrected.

## Slide 16: Second Words of Caution
Users of ns are responsible for verifying for themselves that their simulations are not invalidated by bugs. We are working to help the user with this by significantly expanding and automating the validation tests and demos.

## Slide 17: Third Words of Caution
Similarly, users are responsible for verifying for themselves that their simulations are not invalidated because the model implemented in the simulator is not the model that they were expecting. The ongoing ns Notes and Documentation should help in this process.

## Slide 18: Workshop Goals
Caution to be taken
Existing capability
Design and implementation
Extendibility
Promote sharing

## Slide 19: Outline: This Morning
Introduction
  the project, the software, the philosophy
  software architecture
  installation and getting started
tcl/otcl/ns-2 fundamentals
  programming tcl/otcl
  programming ns-2 simulation scripts
Example scripts
  TCP, web traffic, RED, multicast, wireless

## Slide 20: Object-Oriented
Reusability
Maintainability
Careful planning ahead
Performance

## Slide 21: C++ and otcl Separation
C++ for data
  per packet action
otcl for control
  periodic or triggered action
Compromize between composibility and speed
Learning & debugging

## Slide 22: otcl and C++: The Duality
C++
otcl

## Slide 23: tcl Interpreter With Extents
otcl: Object-oriented support
tclcl: C++ and otcl linkage
Discrete event scheduler
Data network components
tcl8.0
otcl
tclcl
ns-2
Event
Scheduler
Network
Component

## Slide 24: Installation
Getting the pieces
  (tcl/tk8.0), otcl, tclcl, ns-2, (and nam-1)
http://www.isi.edu/nsnam/ns/
ns-users@isi.edu
  ns-users-request@isi.edu
  ‘subscribe ns-users’ in body
ns-announce@isi.edu

## Slide 25: Hello World - Interactive Mode
swallow 71% ns
% set ns [new Simulator]
_o3
% $ns at 1 “puts \“Hello World!\””
1
% $ns at 1.5 “exit”
2
% $ns run
Hello World!
swallow 72%

## Slide 26: Hello World - Passive Mode
simple.tcl
  set ns [new Simulator]
  $ns at 1 “puts \“Hello World!\””
  $ns at 1.5 “exit”
  $ns run
swallow 74% ns simple.tcl
Hello World!
swallow 75%

## Slide 27: Outline: This Morning
Introduction
  the project, the software, the philosophy
  software architecture
  installation and getting started
tcl/otcl/ns-2 fundamentals
  programming tcl/otcl
  programming ns-2 simulation scripts
Example scripts
  TCP, web traffic, RED, multicast, wireless

## Slide 28: Fundamentals
tcl
otcl
  ftp://ftp.tns.lcs.mit.edu/pub/otcl/doc/tutorial.html
ns-2
  http://www.isi.edu/nsnam/ns/ns_doc.ps.gz
  http://www.isi.edu/nsnam/ns/ns_doc.pdf
  http://www.isi.edu/nsnam/ns/doc/index.html

## Slide 29: Basic tcl
proc test {} {
set a 43
set b 27
set c [expr $a + $b]
set d [expr [expr $a - $b] * $c]
for {set k 0} {$k < 10} {incr k} {
if {$k < 5} {
puts “k < 5, pow= [expr pow($d, $k)]”
} else {
puts “k >= 5, mod= [expr $d % $k]”
}
}
}
test

## Slide 30: Basic otcl
Class mom
mom instproc init {age} {
$self instvar age_
set age_ $age
}
mom instproc greet {} {
$self instvar age_
puts “$age_ years old mom: How are you doing?”
}
Class kid -superclass mom
kid instproc greet {} {
$self instvar age_
puts “$age_ years old kid: What’s up, dude?”
}
set a [new mom 45]
set b [new kid 15]
$a greet
$b greet

## Slide 31: Basic ns-2
Creating the event scheduler
[Tracing]
Creating network
Computing routes
Creating connection
Creating traffic
Inserting errors

## Slide 32: Creating Event Scheduler
Create scheduler
  set ns [new Simulator]
Schedule event
  $ns at <time> <event>
  <event>: any legitimate ns/tcl commands
Start scheduler
  $ns run

## Slide 33: Tracing
Trace packets on all links
  $ns trace-all [open test.out w]
<event> <time> <from> <to> <pkt> <size>--<flowid> <src> <dst> <seqno> <aseqno>
  + 1 0 2 cbr 210 ------- 0 0.0 3.1 0 0
  - 1 0 2 cbr 210 ------- 0 0.0 3.1 0 0
  r 1.00234 0 2 cbr 210 ------- 0 0.0 3.1 0 0
Trace packets on all links in nam-1 format
  $ns namtrace-all [open test.nam w]
Right after ‘set ns [new Simulator]’

## Slide 34: Creating Network
Nodes
  set n0 [$ns node]
  set n1 [$ns node]
Links & Queuing
  $ns duplex-link $n0 $n1 <bandwidth> <delay> <queue_type>
  <queue_type>: DropTail, RED, CBQ, FQ, SFQ, DRR

## Slide 35: Tracing Specific links
$ns trace-queue $n0 $n1
$ns namtrace-queue $n0 $n1

## Slide 36: Creating Network: LAN
LAN
  $ns make-lan <node_list> <bandwidth> <delay> <ll_type> <ifq_type> <mac_type> <channel_type>
  <ll_type>: LL
  <ifq_type>: Queue/DropTail,
  <mac_type>: MAC/802_3
  <channel_type>: Channel

## Slide 37: Computing routes
Unicast
  $ns rtproto <type>
  <type>: Static, Session, DV, cost, multi-path

## Slide 38: Creating Connection: UDP
UDP
  set udp [new Agent/UDP]
  set null [new Agent/NULL]
  $ns attach-agent $n0 $udp
  $ns attach-agent $n1 $null
  $ns connect $udp $null

## Slide 39: Creating Connection: TCP
TCP
  set tcp [new Agent/TCP]
  set tcpsink [new Agent/TCPSink]
  $ns attach-agent $n0 $tcp
  $ns attach-agent $n1 $tcpsink
  $ns connect $tcp $tcpsink

## Slide 40: Creating Traffic: On Top of TCP
FTP
  set ftp [new Application/FTP]
  $ftp attach-agent $tcp
  $ns at <time> “$ftp start”
Telnet
  set telnet [new Application/Telnet]
  $telnet attach-agent $tcp

## Slide 41: Creating Traffic: On Top of UDP
CBR
  set src [new Application/Traffic/CBR]
Exponential or Pareto on-off
  set src [new Application/Traffic/Exponential]
  set src [new Application/Traffic/Pareto]

## Slide 42: Creating Traffic: Trace Driven
Trace driven
  set tfile [new Tracefile]
  $tfile filename <file>
  set src [new Application/Traffic/Trace]
  $src attach-tracefile $tfile
<file>:
  Binary format
  inter-packet time (msec) and packet size (byte)

## Slide 43: Inserting Errors
Creating Error Module
  set loss_module [new ErrorModel]
  $loss_module set rate_ 0.01
  $loss_module unit pkt
  $loss_module ranvar [new RandomVariable/Uniform]
  $loss_module drop-target [new Agent/Null]
Inserting Error Module
  $ns lossmodel $loss_module $n0 $n1

## Slide 44: Network Dynamics
Link failures
  route changes reflected automatically
  can emulate node failure

## Slide 45: Four Models
$ns rtmodel-at <time> <up|down> $n0 $n1
$ns rtmodel Trace <config_file> $n0 $n1
$ns rtmodel <model> <params> $n0 $n1
<model>: Deterministic, Exponential
<params>: [<start>] <up_interval> <down_interval> [<finish>]

## Slide 46: Outlines
Essentials
Getting Started
Fundamental tcl, otcl and ns-2
Case Studies - TCP, web traffic, RED

## Slide 47: Case Studies
TCP (tcp.tcl)
Web (web.tcl & dumbbell.tcl)
Queuing - RED (red.tcl)

## Slide 48: Visualization Tools
nam-1 (Network AniMator Version 1)
xgraph

## Slide 49: Basic ns-2: Special Topics
multicast support
application-level support
wireless support

## Slide 50: Multicast - 5 components
enable multicast capability
configure multicast routing
create a multicast group/sender
create a multicast receiver
attach traffic source

## Slide 51: Enabling multicast capability
set ns [new Simulator -multicast on]
or $ns multicast (right after [new Simulator])

## Slide 52: Configuring multicast routing
$ns mrtproto <type>
<type>: CtrMcast, DM, ST, BST

## Slide 53: Creating a multicast group
set udp [new Agent/UDP]
$ns attach-agent $n0 $udp
set group [Node allocaddr]
$udp set dst_addr_ $group

## Slide 54: Creating a multicast receiver
set rcvr [new Agent/NULL]
$ns attach-agent $n1 $rcvr
$ns at <time> “$n1 join-group $rcvr $group”

## Slide 55: Attaching a traffic source
set cbr [new Application/Traffic/CBR]
$cbr attach-agent $udp
$ns at <time> “$cbr start”

## Slide 56: Application - 2 components
two-way TCP
Application/TcpApp

## Slide 57: Application: Two-way TCP
FullTcp connection
  set tcp1 [new Agent/TCP/FullTcp]
  set tcp2 [new Agent/TCP/FullTcp]
  $ns attach-agent $n1 $tcp1
  $ns attach-agent $n2 $tcp2
  $ns connect $tcp1 $tcp2
  $tcp2 listen

## Slide 58: Application: TcpApp
User data transfer
  set app1 [new Application/TcpApp $tcp1]
  set app2 [new Application/TcpApp $tcp2]
  $app1 connect $app2
  $ns at 1.0 “$app1 send <data_byte> \”<ns-2 command>\””
  <ns-2 command>: will be executed when received at the receiver TcpApp

## Slide 59: Wireless - 5 components
setup
node configuration
  layer 3-2, layer 1, tracing, energy
node coordinates
node movements
nam tracing

## Slide 60: Setup
set ns [new Simulator]
set topo [new Topography]
$topo load_flatgrid <length> <width>

## Slide 61: Node Configuration: Layer 3-2
$ns node-config
  adhocRouting <adhoc routing type>
  llType LL
  ifqType Queue/DropTail/PriQueue
  ifqLen <queue length>
  macType Mac/802_11
<adhoc routing type>: DSDV, DSR, TORA, AODV

## Slide 62: Node Configuring: Layer 1
$ns node-config
  phyType Phy/WirelessPhy
  antType Antenna/OmniAntenna
  propType <propagation model>
  channelType Channel/WirelessChannel
  topoInstance $topo
<propagation model>: Propagation/TwoRayGround, Propagation/FrissSpaceAttenuation

## Slide 63: Node Configuration: Tracing
$ns node-config
  agentTrace <ON or OFF>
  routerTrace <ON or OFF>
  macTrace <ON or OFF>

## Slide 64: Node Configuration: Energy
$ns node-config
  energyModel EnergyModel
  initialEnergy <total energy>
  txPower <energy to transmit>
  rxPower <energy to receive>

## Slide 65: Creating Nodes
set mnode [$ns node]

## Slide 66: Node Coordinates
$mnode set X_ <x>
$mnode set Y_ <y>
$mnode set Z_ 0

## Slide 67: Node Movement
Disable random motion
  $mnode random-motion 0
Specified
  $ns at 1.0 “$mnode setdest <x> <y> <speed>”
Random
  $ns at 1.0 “$mnode start”

## Slide 68: Tracing
at the beginning
  $ns namtrace-all-wireless [open test.nam w] <length> <width>
initialize nodes
  $ns initial_node_position $mnode 20
at the end
  $ns at <end time> “$ns nam-end-wireless <end time>”

## Slide 69: Case Studies
multicast (mcast.tcl)
wireless (wireless-udp.tcl, wireless-tcp.tcl)

## Slide 70: Basic ns-2: Not Covered
mobile IP
satellite
DiffServ
emulation

## Slide 71: Lab Exercises
Bookmark
  http://www.tik.ee.ethz.ch/~huang/ns-tutorial/ftw-tutorial.html
Setup
  work under these 1/ 2/,...20/
  exec nam -a out.nam